## Slide 1: The Smart Resue Boat - Robotics
Presented by – COHNDSE-017
COHNDSE-021
Lecturer- MR.Vimukuthi

## Slide 2: Agenda
The Problem & Solution Building confidence – Slide 01
System Hardware Architecture – Slide 02
Wiring & Connection Summary – Slide 03
Software Logic: The "Priority" Loop – Slide 04
Autopilot & Steering Logic – Slide 05
Critical Technical Challenges Overcome – Slide 05
Conclusion & Future Scope – Slide 06

## Slide 3: The Problem & Solution

## Slide 4: The Problem:
Traditional remote-controlled rescue boats require constant human line-of-sight and are prone to collisions in debris-heavy water.

## Slide 5: Our Solution:
A smart vessel that can:
Be controlled via Bluetooth.
Automatically stop for obstacles.
"Return to Home" using GPS coordinates with zero user input

## Slide 6: System Hardware Architecture

## Slide 7: Hardware components and their usecases:
Microcontroller: Arduino Nano.
Communication: HC-05 Bluetooth (Serial control).
Navigation: NEO-6M GPS Module (Coordinate tracking).
Sensing: HC-SR04 Ultrasonic Sensor (Collision avoidance)
Output: L298N/L293D Driver (Propulsion) & MG995 Servo (Steering).

## Slide 8: Wiring & Connection Summary

## Slide 9: Wiring & Connection Summary
Serial Communication: * Bluetooth: Pins 2 (RX) / 3 (TX)
GPS: Pins A0 (RX) / A1 (TX)
Peripheral Control:
Ultrasonic: Pins 12 (Trig) / 13 (Echo)
Actuators: Pin 11 (Servo), Pins 5/6 (DC Motor)
Feedback: Pin 10 (Buzzer)

## Slide 10: : Software Logic: The "Priority" Loop
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 11: The "Priority" Loop
Level 1 (Highest): Safety. Ultrasonic check runs every cycle. If Distance < 25cm $\rightarrow$ EmergencyStop().
Level 2: User Input. Bluetooth commands take priority over autopilot to allow manual override.
Level 3: Navigation. GPS data is parsed in 80ms windows to prevent "Serial Blocking."

## Slide 12: Autopilot & Steering Logic
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 13: Autopilot & Steering Logic
Targeting: Saves current $Lat/Lng$ when "H" (Home) is pressed.
Heading Calculation: Compares current GPS heading with the bearing to the target.

## Slide 14: Terminal response when GPS engaged

## Slide 15: Challenges Overcome
Serial Conflicts: Solved the "Freezing" issue by optimizing the GPS listening window to 80ms.
Mechanical Reliability: Implemented a "Kickstart" function to ensure the propeller starts under water resistance.
Logic Stability: Filtered out "Ghost Echoes" (0cm readings) from the ultrasonic sensor to prevent false stops.

## Slide 16: Some of the existing challenges and issues
1. The "Indoor" Barrier (Most Common) :The module's red LED is solid or off, and the serial monitor says "No GPS Lock.“
The Fix: You must take the boat outside under an open sky.
2. The "Serial Conflict" (Software Issue) : When the GPS sends a long string of data, it blocks the Bluetooth. When the Bluetooth sends data, it blocks the GPS.

## Slide 17: Future Enchancement
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 18: Enhancements planned to be done in future
Addition of an NRF24L01 for kilometer-range communication.
Integrating a First-Person View (FPV) camera for remote rescue.
Implementation of solar charging for extended battery life.
Integrating Compass/Magnetometer (HMC5883L / QMC5883L) instead of NEO-6M GPS module – gives the boat the sense of direction even when staying still
GPS + RTK (Real-Time Kinematics) – unlike standard NEO-6M which is accurate for only about 2.5-5m this sensor is accurate to 2cm

## Slide 19: Thank you
COHNSE252F-017 : E.Danushyan
COHNDSE252F-019 : Rasindhu Yasas